►	TIP & TRICK :       [Foefjes en wetenswaardigheden, eventueel uitgelegd met voorbeelden.]

T&T 0017  #  FSNavigator switches in je cockpit bouwen.  [ voor gevorderden ]

1:	Start  je Browser en ga naar pagina  www.fsnavigator.com  en kies voor de optie DOWNLOAD

Onderaan de pagina zie je Freeware Gauges.

2:	Download de file fsnhsi13.zip  313Kb

3:	Pak deze uit in je Map C:\TEMP

4:	Kopieer de 7  *.GAU  files  naar je  \FS2004\Gauges  MAP

5:	Print de file FSNAV.ReadMe.txt uit.

6:	Ga nu naar de Panel MAP van het vliegtuig waarin je deze Switches wilt bouwen.

Als voorbeeld neem ik de panel.cfg van de standaard B737-400

7:	Kopieer eerst de te bewerken Panel.cfg  file naar bv Panel_ORG.cfg

8:	Open met kladblok  de file  Panel.cfg.

9:	Ga naar [window00]

Vervang de regel

gauge31=737-400!Nav GPS Switch, 306, 17

door

gauge31=FSNAV.GPS_Switch, 302, 17, 30

10:	Plaats onder aan de [window00] gauges de regels

gauge38=FSNAV.FlyPlan, 120, 10, 20

gauge39=FSNAV.FlyMode, 140, 10, 20

gauge40=FSNAV.NextWP, 160, 10, 20

gauge41=FSNAV.PrevWP, 180, 10, 20

gauge42=FSNAV.FlyHold, 200, 10, 20

[denk om de opvolgende gauge-nummereing !!!]

USAGE:

All FSNav functions are not available until you activate

FSNav the first time  [F9]  once in a FS session.

The Switch Set has five switches to control FSNav:

PLAN - toggles 'Fly Flightplan' on/off

M1M2 - toggles the FMS options 'Mode1' to 'Mode2' and back

HOLD - toggles 'Fly Holding' on/off

PREV - selects the previous waypoint of the flightplan (if

available)

NEXT - selects the next waypoint of the flightplan (if

available)

The intention of the M1M2 switch is to activate the option

'Set and Hold Heading' only in one of the two modes. If 'Fly

Flightplan' is activ you can change from manual to

automatic flight by switching M1M2.